## Slide 1: ROSA Operating system
Adding extended functionality to an existing OS
Jukka Mäki-Turja

## Slide 2: Backstory to ROSA – Real-time OS for AVR32
We are a small company that has developed a cooperative non-premptive little OS for AVR32
Our OS has been used in small electronic devices such as micros, vacuum cleaners, landry machines,…
  Has been sufficient so far
Now we got a new customer that has higher demands on both functionality and safty criticality
  Real-time operating system for a wheel-loader
  Up to 5 ECUS – Electronic control units
  Each ECU has ca a dozen tasks

## Slide 3: Current OS
All tasks are created and installed before system is created
  EXECTASK
  TCBLIST
A cooperative OS
  Only one system call – ROSA_yield()
    Relinquishes control of CPU
    Next task in TCBLIST is chosen for execution

## Slide 4: Extended functionality
Fixed priority scheduler
To be able to realize periodic activation and preemptive scheduling of tasks. System clock ticks and delay functionality have to be added
Dynamic creation and termination of tasks
Binary semaphore handling
Synchronization protocol

## Slide 5: Fixed priority scheduler
The scheduler in ROSA is too simple for our needs
  It is a cooperative non-premptive one
It is required to implement the Fixed Priority Preemptive Scheduling algorithm (FPPS)
Arrangements for this in the code would be really helpful

## Slide 6: Pre-emptive scheduling
The periodicity of our tasks should be controlled in a better way
Therefore it is needed to have clock tick interrupts that keeps track of system time
  The resolution of clock ticks should be in the millisecond range.
Both relative and absolute delay functionality should be provided
  System calls for both are needed

## Slide 7: Dynamic creation and termination of tasks
We would like to be able to create and remove tasks on the fly
  That is, during run-time

## Slide 8: Semaphores
Today we have no option to protect critical code section and access to shared resources
Thus, semaphores has to be included in ROSA.
With semaphores we can foresee some problems with deadlocks
and unbounded priority inversion
To solve those problems would like to use the immediate inheritance protocol IPCP

## Slide 9: Documentation
ROSA_doc.pdf – Extensive description of current ROSA
ROSA_API_appendix.pdf – Complete API of current ROSA
Order.pdf – The order for extending ROSA
ROSA_timerInterrupt.pdf – More on context switch and timer interrupts

## Slide 10: Questions?